Scrypt Hashing ASIC
Eric Schrock
Kyle Chynoweth

---
Scrypt Hashing
- Primary purpose for mining cryptocurrency
  - Hashes 80B of input into a 32B key
  - Compares the key to a “target” hash
  - If key is less than the target, submit confirmed hash
    - This would be done by transmitting the hash data to the “blockchain”. Done through driver, not through device.
- Operates in parallel with other scrypt devices via i2c

---
System Diagram

---
Architecture Diagram

---
Device Operation
[insert flowchart]

---
I2C Transceiver

---
Scrypt_Top

---
PBKDF2_80_80_128

---
PBKDF2_80_128_32

---
HMAC_SHA256_164
HMAC_SHA256_212

---
HMAC_SHA256_32

---
SHA256

---
Scypt_SMix

---
Scrypt_Blockmix

---
Salsa20_8

---
Budget Overview
- 54000000 um^2
- Target frequency: 1/(6ns)
- Primary area:
  - SHA256 internal registers: 27 000 000
  - Scrypt 128kB scratchpad: 9 600 000
- Primary Timing
  - SRAM -> mux -> FF: 5.5ns